## Slide 1: Hardware Description Language Computing Units
2024.03.15 (Friday)

## Slide 2: Outlines
Verilog HDL
Labs: Computing Units

## Slide 3: References
Class: Digital Systems Design and Experiments (https://ocw.snu.ac.kr/node/2390)
Books: Digital System Designs and Practices: Using Verilog HDL and FPGAs @Willy 2008

## Slide 4: FPGA design flow
Function Specification
RTL design
Logic Synthesis
Implementation
FPGA programming
Behavioral Simulation
Timing Analysis
Tiny-YOLO3-AIX2022
Generate bitstream
Xilinx IP
Power, Resource (DSPs, LUTs)
Function simulation
Text editor: vim, notepad++, VS code
RTL simulator: ModelSim, ISE, Vivado
FPGA Implementation (ISE, Vivado)
Synthesize the design
Implementation: mapping, placement and routing
Optimization
Analyze timing, power, resources

## Slide 5: Hardware Description Language (HDL)
HDL is an acronym of Hardware Description Language
Two most commonly used HDLs:
  Verilog HDL (also called Verilog for short)
  VHDL (Very high-speed integrated circuits HDL)
Features of HDLs:
  Design can be described at a very abstract level.
  Functional verification can be done early in the design cycle.
  Designing with HDLs is analogous to computer programming.

## Slide 6: Modules – Hardware Module Concept
The basic unit of a digital system is a module.
Each module consists of:
  a core circuit (called internal or body) ---performs the required function
  an interface (called ports) ---carries out the required communication between the core circuit and outside.

## Slide 7: Modules –Verilog HDL modules
module---The basic building block in Verilog HDL.
  It can be an element or a collection of lower-level design blocks.

## Slide 8: Lexical Conventions
Sized number: <size>`<base format><number>
  4`b1001 ---a 4-bit binary number
  16`habcd ---a 16-bit hexadecimal number
Unsized number: `<base format><number>
  2007 ---a 32-bit decimal number by default
  `habc ---a 32-bit hexadecimal number
x or z values: x denotes an unknown value; z denotes a high impedance value.
Negative number: -<size>`<base format><number>
  -4`b1001 ---a 4-bit binary number
  -16`habcd ---a 16-bit hexadecimal number
”_” and “?”
  16`b0101_1001_1110_0000
  8`b01??_11?? ---equivalent to a 8`b01zz_11zz

## Slide 9: Data types
A net variable
  can be referenced anywhere in a module.
  must be driven by a primitive, continuous assignment, force … release, or module port.
A variable
  can be referenced anywhere in a module.
  can be assigned value only within a procedural statement, task, or function.
  cannot be an input or inout port in a module.

## Slide 10: Port Declaration
Port Declaration
  input: input ports.
  output: output ports.
  inout: bidirectional ports
Port Connection Rules
  Named association
  Positional association

## Slide 11: Module Modeling Styles
Structural style
Dataflow style
Behavioral or algorithmic style
Mixed style
In industry, RTL (register-transfer level) means
  RTL = synthesizable behavioral + dataflow constructs

## Slide 12: Structural modeling
Structural style
  Gate level comprises a set of interconnected gate primitives.
  Switch level consists of a set of interconnected switch primitives.
Hierarchical design

## Slide 13: Dataflow modeling
Dataflow style specifies the dataflow (i.e., data dependence) between registers.
Use a set of continuous assignment statements
  assign [delay] l_value = expression
  delay: the amount of time between a change of operand used in expression and the assignment to l-value.
Continuous statement in a module execute concurrently regardless of the order they appear.

## Slide 14: Behavioral modeling
Use two procedural constructs: initial and always
initial statement
  Executed only once at simulation time 0
  Used to set up initial value of variable data types
always statement
  Executed repeatedly
At simulation time 0, both initial and always statements are executed concurrently.

## Slide 15: Mixed-Style Modeling
Mixed style is the mixing use of above three modeling styles.
  Commonly used in modeling large designs.
structural
dataflow
behavioral

## Slide 16: Simulation
Design
Simulation
Verification
Stimulus block: testbench
Unit under test (UUT)
Design under test (DUT)

## Slide 17: System Tasks for Simulation
$display displays values of variables, string, or expressions
  $display(ep1, ep2, …, epn);
  ep1, ep2, …, epn: quoted strings, variables, expressions.
$monitor monitors a signal when its value changes.
  $monitor(ep1, ep2, …, epn);
$monitoton enables monitoring operation.
$monitotoff disables monitoring operation.
$stop suspends the simulation.
$finish terminates the simulation.

## Slide 18: Time Scale for Simulations
Time scale compiler directive
  `timescale time_unit / time_precision
The time_precision must not exceed the time_unit.
Example:
  with a timescale 1 ns/1 ps, the delay specification #15 corresponds to 15 ns.
It uses the same time unit in both behavioral and gate-level modeling.
For FPGA designs, it is suggested to use ns as the time unit.

## Slide 19: Outlines
Verilog HDL
Labs: Computing Units

## Slide 20: Labs
Lab 1: DSP
  How to use Vivado IP integrator to generate a DSP?
  How to test a DSP unit?
Lab 2: MAC
  Multipliers and an adder tree
  MAC
Lab 3: Computing units

## Slide 21: Lab 1: DSP
Build a multiplier based on a DSP generated by Vivado IP generator
  Generate a DSP
  Use it to build a multiplier
Make a testbench
  Test the multiplier

## Slide 22: Creating a DSP using Xilinx IP generator
Click “IP Catalog” on Vivado
Search “DSP”
Choose “DSP48 Marco” and double click on it
1
2
3

## Slide 23: Creating a DSP using Xilinx IP generator
The name of the generated DSP
Ports of the DSP
Inputs:
  CLK
  A[17:0], B[17:0]
  C[47:0]
Output:
  P[47:0]
DSP formula
P = A* B+C

## Slide 24: DSP configuration
We can choose a specific formula
Pipeline registers (4-cycle delay between an input and an output)

## Slide 25: Creating a DSP using Xilinx IP generator
Click “OK” and then “Generate” on the popup window
  A DSP is generated
Click
Hardware resource
One DSP is used

## Slide 26: Multiplier (mul.v)
Choose “Add sources” >> “Add or create design sources” >> Click “Next”

## Slide 27: Multiplier (mul.v)
Click “Create File” >> Make a file name “mul” in “Verilog” >> click “OK”
Note: the “mul” code is given.
1
2
3

## Slide 28: Multiplier (mul.v)
  Inputs:
    clk // Clock
    w[7:0] // Weight
    x[7:0] // Input pixel
  Output:
    y[15:0] // Product
  A DSP instance
  Make inputs and outputs for the DSP
  2’s complement for a negative number
  Negative
  Positive

## Slide 29: Testbench (mul_tb.v)
Design under test:
multiplier (mul)
Clock: 100MHz
(Period = 10ns)
Time scale: 1ns
A clock signal is defined in an “initial” block
Initialized at 1
State is changed at every 5ns
Registers (e.g. clk, w, x) are connected to the inputs
A wire (e.g., y) is connected to the output

## Slide 30: Testbench (mul_tb.v)
Initialized states
Set all registers to default values
Generate test cases in 16 cycles
w: 4
x: 0 -> 1 -> 2 -> … -> 15

## Slide 31: Waveform
In Tab “Simulation”, click on “run simulation” >> “Run behavioral simulation”
Visualize the waveform
  Weight (w) is set to 4 in 16 cycles (e.g., 70~230ns)
  During the 16 cycles, x is set from 0 to 15
  The result (y) is 0, 4, …, 60
  For a given input, its output comes out after 4 cycles (e.g., DSP’s pipelined registers)

## Slide 32: Lab 2: MAC
Build a MAC
  Use multiple multipliers
  Adder tree
Make a testbench
  Test the MAC

## Slide 33: DNN accelerator
Processing Element (PE) Array
  An array of multiplication and accumulation (MAC).
  Perform convolution operations.
  Computing unit or “ALU” of a DNN accelerator
On-chip buffers (Weight/Input/Output)
Input Fetcher
Norm/Activation
Weight Fetcher
Processing Elements (PEs)
Adder Tree
…
PE
BUS
Computing
Elements

## Slide 34: MAC
MAC is a module that performs many multiplications and accumulations in parallel.
Review: convolution
  From this example, to calculate output pixel A, we need to calculate:
  (a*1 + b*2 + … + m*9) + (a’*1’ + b’*2’ + … + m’*9’) + … + (a’’*1’’ + b’’*2’’ + … + m’’*9’’)
  lots of multiplication / accumulation!
a’
b’
c’
a’’
b’’
c’’
1’
2’
3’
1’’
2’’
3’’
9’’
6’’

## Slide 35: A simple MAC
In this tutorial, we will give and explain an example MAC module that calculates 16 multiplications and accumulations every cycle.
Inputs are 8 bit 2’s complement numbers
and the output is a 20 bit 2’s complement number
weight
weight
weight
input
input
input
output
MAC

## Slide 36: A simple MAC
Compute a sum of 16 products
Pseudo code
// N multipliers
// N/2 adders
// N/4 adders
// N/4 adders
// N/4 adders
// Output

## Slide 37: MAC (mac.v)
Compute a sum of 16 products
Ports
  clk, rstn: clock and reset signals
  vld_i: a valid signal for inputs (e.g., win, din)
  Inputs win, din
    win[7:0] = , din[7:0] =
    win[15:8] = , din[15:0] =
    …
  Outputs
    Accumulated result (acc_o)
    A valid signal (vld_o)

## Slide 38: Multiplication (mac.v)
Compute a sum of 16 products
Internal signals
16 multipliers running in parallel
win[7:0] =
din[7:0] =
win[127:120] =
din[127:120] =

## Slide 39: Accumulation (mac.v)
Compute a sum of 16 products
Pseudo code
Internal signals

## Slide 40: Accumulation (adder_tree.v)
Compute a sum of 16 products

## Slide 41: Delays
Calculating delayed valid signals
vld_i: when high, indicates that win and din are valid inputs, and must be calculated
Delays in the adder tree (adder_tree.v)
  vld_d: an internal variable to calculate the timing for vld_o to be high
  vld_o: when high, indicates that output acc_o is a valid calculation result

## Slide 42: Test bench (mac_tb.v)
Design under test: mac
Time scale: 1ns
Registers (e.g. clk, win, din) are connected to the inputs
Wires (e.g., acc_o, vld_o) are connected to the output
Clock: 100MHz
A clock signal is defined in an “initial” block
Initialized at 1
State is changed at every 5ns

## Slide 43: Test bench (mac_tb.v)
Initialized states
Set all registers to default values
Generate test cases in 16 cycles
w: 4
x: 0 -> 1 -> 2 -> … -> 15
Note: we have 16 weights and 16 inputs now.

## Slide 44: Waveform

## Slide 45: Waveform
Visualize the waveform
  Weight (w) is set to 4 in 16 cycles (e.g., 70~230ns)
  During the 16 cycles, x is set from 0 to 15
  The result (y) is 0, 4, …, 60
  For a given input, its output comes out after 4 cycles (e.g., DSP’s pipelined registers)

## Slide 46: Waveform
Visualize the waveform
  Weight (w) is set to 4 in 16 cycles (e.g., 70~230ns)
  During the 16 cycles, one input is set from 0 to 15
  The result (acc_o) is 0, 64, …, 960
  For a given input, its output comes out after 8 cycles

## Slide 47: Lab 3: Convolutional layer (Practice)
Convolutional layer
  Use four MAC modules
  Initialize four sets of filters
  Read an image from file
  Do convolution

## Slide 48: Convolutional layer (cnv_tb.v)
Parameters for an image file, e.g., WIDTH, HEIGHT, file location (INFILE), frame/image size
A buffer to store an image (in_img)
Internal signals
  clk, rstn,
  vld_i, din[127:0]
  Four sets of filters win[0:3][127:0]
  acc_o[0:3][19:0]
  vld_o[0:3]

## Slide 49: Convolutional layer (cnv_tb.v)
There are four MAC instances
Each module:
  Uses one set of convolutional filters, e.g., win
  Outputs a specific acc_o

## Slide 50: Convolutional layer (cnv_tb.v)
Read the hex file into a buffer
Initialize four set of convolutional filters
Come from a quantized model

## Slide 51: Waveform
Make code to generate din